## Slide 1: FactoryTalk ® TeamONE™
The App for team productivity - Architecture Examples
October 4th, 2016

## Slide 2: FactoryTalk ® TeamONE™
In this document there are three (3) options of network setups that will help you realize the benefits of the TeamONE app. You will be able to use different modules depending on the architecture you select.
  Network Architecture Example 1 – Collaboration Modules. You need internet access for these modules.
  Network Architecture Example 2a & 2b – Device Troubleshooting Modules. You need access to the plant network for these modules.
  Network Architecture Example 3 – All modules through a unified in band setup. This setup requires access to both the internet and the plant network.
If you have any questions or comments just email ramobilesupport@ra.rockwell.com and we’ll help you out!

## Slide 3
Download App on cell or Wi-Fi enabled device
1
Create OR join team
2
Use with internet
3
FUNCTIONAL MODULES
ARCHITECTURE 1
TeamONE syncs to team DB in FactoryTalk Cloud!
Login and team creation done online.

## Slide 4: Network Architecture Example 1
Collaboration Modules only - The following examples show sample network architectures of how you can achieve this
IT Wifi
Office Laptop
WiFi iOS or Android device (refer to supported device list) with cellular data service.
WiFi only iOS or Android device (refer to supported device list)
TeamONE
Preview release module details:
Chat– Chat with any team member.
Teamboard – Post to all team members
Incident – Record issues with machines or products
Pinboard – Favorite board of incidents
KnowledgeBase – Automatic login to KB for articles.
SmartPhone WiFi only devices for Project Stanton
(Collaboration only)
SmartPhone cell service devices for Project Stanton
(Collaboration only)
Option 1
Option 2

## Slide 5
Download App on cell or Wi-Fi enabled device
1
Create team of one (1) or more
2
Connect to an in panel wifi network
3
FUNCTIONAL MODULES
ARCHITECTURE 2
Login and team creation done ‘online’. No device data is synced.

## Slide 6: Network Architecture Example 2
Device Modules - The following examples show sample network architectures of how you can achieve this
I/O
Drive
FactoryTalk Client
WGB
AP
Controller
Distribution switch
Controller
Controller
Cell/Area Zones - Levels 0-2 (Lines, Machines, Skids, Equipment)
IES
IES
IES
IES
IES
Laptop for Programming (Studio 5000)
Recommended - WiFi only iOS or Android device (refer to supported device list)
WiFi iOS or Android device (refer to supported devices list) with cellular data service. All modules will be available BUT this will NOT SYNC ANY DEVICE DATA TO THE CLOUD and the user has to disconnect from the local Wi-Fi for sync to occur.
TeamONE
TeamONE module details using WiFi only:
Device Health – Connect to any Ethernet IP device and read high level status. Parameter tab shows up in device details page for Powerflex 525 or 755 only.
Trend – Connect Powerflex 525 or 755 only and do a real time trend of any parameter.
SmartPhone devices for TeamONE
(Monitoring & collaboration)
Option 2a - Autonomous
AP = Access Point (locally managed) recommended MAC filtering, no broadcast SSID, WPA2
I/O
Drive
FactoryTalk Client
WGB
LWAP
Controller
Distribution switch
Controller
Controller
Cell/Area Zones - Levels 0-2 (Lines, Machines, Skids, Equipment)
IES
IES
IES
IES
IES
SmartPhone devices for TeamONE
(Monitoring & collaboration)
Option 2b - Unified
Optional Sync
WLC (Active)
WLC (Standby)
LWAP = Lightweight Wireless Access Point
WLC – Wireless Lan Controller – This manages the security policies, access control, etc. centrally
Laptop for Programming (Studio 5000)
Out of band - ‘In cabinet’ WiFi access point with or without cloud access.
When device disconnects from local Wi-Fi
Optional Sync
When device disconnects from local Wi-Fi

## Slide 7
Setup firewall between OT & IT networks
1
Ensure ports are open for sync & push messaging enabled
2
Add devices to OT wireless network with no SIM chips
3
Download App
4
Create & Join Team
5
Use route to cloud via firewall
6
ARCHITECTURE 3
OT NETWORK
IT NETWORK
DMZ
TeamONE serves as gateway for modules that sync via cloud.
No device data is synced.
FUNCTIONAL MODULES

## Slide 8: Network Architecture Example 3
All modules - The following examples show sample network architectures of how you can achieve this
Enterprise WAN
Firewalls (Active/Standby)
Enterprise Zone: Levels 4-5
I/O
Level 3
Site Operations
Drive
Industrial Demilitarized Zone (IDMZ)
FactoryTalk Client
Internet
External
DMZ / Firewall
WGB
WLC (Active)
WLC (Standby)
LWAP
Controller
Core switches
Distribution switch
Core switches
WLC (Enterprise)
ISE MnT
ISE PAN/PSN
ISE PSN
Controller
Controller
Industrial Zone
Levels 0-3
(Plant-wide Network)
Cell/Area Zones - Levels 0-2 (Lines, Machines, Skids, Equipment)
IES
IES
IES
IES
IES
Laptop for Programming (Studio 5000)
Wi-Fi only iOS or Android device (refer to supported device list)
TeamONE
Port 443 (TeamONE DB sync back and forth to cloud)
Ports 5223, 2195 & 2196 for Apple Push Messaging
Ports 5228,5229,5230 for Google/Android Cloud Messaging
All the devices running the App Platform within the OT network will need to access these ports.
Unified in band setup